## Slide 1
Compressor
Air regulator 1
E-Valve 2
Breathing - Patient
E-Valve 4
UV light
ULPA filter
Dynamic Air Container (Air Cylinder)
If a reliable medical air line is available with enough* pressure, then no compressor is needed.
Air filter 1
Air filter 2
“Pandemic” ventilator – Minimal design
Air system diagram
Design by Marco Mascorro. @Mascobot
Email: m@marcomascorro.com
For educational purposes only.
Use at your own risk.
E-Valve 1
E-Valve 6
Pressure-controlled Oxygen
Line denotation
Clean air
Contaminated air
Oxygen
Notes:
Oxygen input needs to be “flow-positive” into the system.
If oxygen is not used, E-Valve-6 can be removed, and its line needs to be sealed/closed.
Disclaimer: Non-FDA approved. This product is not intended to diagnose, treat, cure, or prevent any disease.
E-Valve 3
E-Valve 5
Version: V0.15
Air regulator 2
(to control patient breathing pressure/speed )
Limit Switch 2
Limit Switch 1
Adjustable position (to control air tank size)
Joints
Filtering

## Slide 2
Dynamic Air Container (Air Cylinder)
“Pandemic” ventilator
Electric system diagram
12 VDC
N.C.
N.O.
N.C.
N.O.
E-Valve 2
N.C.
E-Valve 4
N.C.
E-Valve 1
N.C.
E-Valve 3
N.C.
SW 1
SW 2
C.
N.C.
N.O.
12V Coil
Relay 1
C.
N.C.
N.O.
Relay 2
Switch
Notes:
If oxygen is not used, don’t install E-Valve 6
Nomenclature:
N.C. - ”Normally Closed”
N.O. - ”Normally Open”
(Optional 12V battery )
Fuse
87a - White
87 - Blue
86 -Yellow
87 - Red
12V Coil
87 - Red
86 -Yellow
87a - White
87 - Blue
30 - Black
30 - Black
Version: V0.15
Design by Marco Mascorro. @Mascobot
Email: m@marcomascorro.com
For educational purposes only.
Use at your own risk.
Disclaimer: Non-FDA approved. This product is not intended to diagnose, treat, cure, or prevent any disease.
E-Valve 6
N.C.
E-Valve 5
N.C.